## Slide 1: Review RT-comments for draft-mtaillon-mpls-summary-frr-rsvpte

## Slide 2: Comments[Greg]
The document intended to update RFC 4090 but I don't find that being stated clearly and the proposed procedures are not related to procedures defined in RFC 4090 for facility protection with a bypass tunnel. I would expect that the draft updates procedures discussed in Section 6.4 of RFC 4090.
Though not clearly stated, it appears that the intention to use the SUMMARY_FRR_BYPASS_ASSIGNMENT is in signaling working path. That appears as implicit implementation requirement towards a PLR to determine MP before forwarding Path message.
Section 2.1.1 states:
The PLR MUST generate a new Message_Identifier each time the
SUMMARY_FRR_BYPASS_ASSIGNMENT subobject contents change; for example,
when PLR changes the bypass tunnel assignment.
My question to Authors How a PLR can update MPs if the LER would not send the Path message? [TS]: The PLR originates a new Path message (that contains the changes in the SFRR BA sub-objs). This is not unusual for RSVP-TE LSP in accordance to rfc3209 section section-4.4.3
AI: quote rfc4090 for clearer example.

## Slide 3: Comments[Mach]
General comments:
Overall, after reading the draft, I think the issue/requirement is valid, the solution is straightforward although the specific extensions need more discussions. The draft is ready to be considered as WG document.
The draft is not clear whether the solution is for P2Pt LSP or P2MP LSP or both. A: P2MP will be addressed in a future revision.
Specific comments:
Section 2.1
When defining the Bypass_Group_Identifier and Summary_FRR_PLR_Generation_Identifier fields, there is few text explain the meaning and purposes, I found some text in the signaling sections about the usage and purpose of the ids, but it's better to add more definition and description text at their definition places to make it clear and easy to read.
In addition, for Summary_FRR_PLR_Generation_Identifier, it does not specify the length.
Bypass_Group_Identifier
Summary_FRR_PLR_Generation_Identifier

## Slide 4: Comments[Mach] - ctd
Section 2.2.1 "The SUMMARY_FRR_BYPASS_ASSIGNMENT subobject is added in the RECORD_ROUTE object prior to adding the node's IP address. A node MUST NOT add a SUMMARY_FRR_BYPASS_ASSIGNMENT subobject without also adding the node's IPv4 or IPv6 subobject.”
What's the reason for that the SUMMARY_FRR_BYPASS_ASSIGNMENT subobject must be added prior to adding the node's IP address? And the above two sentences may bring more difficulties to the implementation, since whether SUMMARY_FRR_BYPASS_ASSIGNMENT is added depends on whether the node's IP is added, but it does requires to add the SUMMARY_FRR_BYPASS_ASSIGNMENT firstly, if later the node's IP address will not be added, is the added SUMMARY_FRR_BYPASS_ASSIGNMENT going to be removed? Seems some rewording needs here.
XXXXXXX differ to Lou’s comments
Section 2.2.2 The MP first ensures the existence of the bypass tunnel and that the Bypass_Group_Identifier is not already active. That is, an LSP cannot join a group that is already active.
What's is called that a Bypass_Group_Identifier is active? Looking through the document, since there is no definition and description about "Bypass_Group_Identifier active".

## Slide 5: Comments[Eric]
I have read this document and I agee with Mach that the issue is valid and the solution is straightforward. I can tell you from experience that this problem needs solving, so I think the document is ready to proceed as a WG draft. There are parts of the document that need some cleanup and I agree with both Mach and Greg that there are parts that are unclear, but that's not a blocker to WG acceptance.

## Slide 6: Comments[Lou]
WRT SUMMARY_FRR_BYPASS_ACTIVE object
RSVP object space is a pretty scarce resource and it seems we have a number of existing objects that could be reused to support transport of the required information. Some candidates include: the Association object with a new association type; or perhaps the PRIMARY_PATH_ROUTE Object with a new C-type. [TS]: rfc6780: “The RSVP ASSOCIATION object was defined in the context of GMPLS- controlled Label Switched Paths (LSPs). In this context, the object is used to associate recovery LSPs with the LSP they are protecting.”
SUMMARY_FRR_BYPASS_ASSIGNMENT subobjects
While RFC4090 makes use of RRO carried information, it does so without changing the RRO format. (At the time, I recall some used this as justification for RRO usage vs introducing new formats.) The new Sos introduce new information and don't seem to be particularly linked to normal RRO operation -- and more significantly really defining new transit-node to transit-node signaling semantics: [TS]: the new SO, is recording local information that if intercepted by another LSR (PLR or MP that understands it) can use it for further summary FRR processing. This resembles to an extent what other RRO SOs do today (e.g. node-id and label Sos) for regular FRR

## Slide 7: Comments[Lou]
The PLR notifies the MP of the bypass tunnel assignment via adding a SUMMARY_FRR_BYPASS_ASSIGNMENT subobject to the RSVP Path message RECORD_ROUTE object … The MP acknowledges the PLR's assignment by signalling a SUMMARY_FRR_BYPASS_ASSIGNMENT subobject within the RSVP Resv messsage RECORD_ROUTE object.
IMO this usage of RRO is really wrong (and is easily broken by application of RRO policies). I think extending an existing object class is a better approach. Extending one of the existing FRR objects would probably be cleanest, but think the authors should consider and propose their preference. [TS]: yes, the comment (about RRO policies) is rightfully correct. .. but also applicable to existing RRO/SO(s) (e.g. node-id and/or label SO) needed for proper FRR too. That said, will discuss extension of an existing (FRR) object amongst the authors for (dis)advantages.

## Slide 8: Comments[Lou]
When [RFC4090] isn't being used, the association between segment recovery LSPs with other LSPs is indicated using the ASSOCIATION object defined in [RFC4872]. The ASSOCIATION object is used to associate recovery LSPs with the LSP they are protecting. Working and protecting LSPs, as well as primary and secondary LSPs, are identified using LSP Status as described in [RFC4872]. The O-bit in the segment flags portion of the PROTECTION object is used to identify when a recovery LSP is carrying the normal (active) traffic.

## Slide 9
mention the bidir-FRR draft